## Slide 1: PORTABLE FIRE EXTINGUISHER TRAINING
Goal
  Provide information on the correct use of portable fire extinguishers
Objective
  To be able to identify the different classes of fires, and select and properly use the appropriate fire extinguisher for each class of fire

## Slide 2: PORTABLE FIRE EXTINGUISHER TRAINING
Introduction
  Fire is a chemical reaction involving the rapid burning of fuel
  Fuel can be any combustible material-solid, liquid or gas.
  Four elements are needed for a fire to occur
    Fuel
    Oxygen (16% or more)
    Heat
    Chemical Reaction

## Slide 3: PORTABLE FIRE EXTINGUISHER TRAINING
Remove any of those factors and the fire cannot occur or will extinguish itself if already burning
The effectiveness of a fire extinguisher on a particular fire depends on:
  The size of the Fire
  The amount and type of agent in the extinguisher
Portable fire extinguishers are effective in putting out small fires
  Care must be taken in their proper selection and use

## Slide 4: PORTABLE FIRE EXTINGUISHER TRAINING
Classes of Fires:
  Class A : Have ordinary combustible materials
    Wood, paper, cloth, rubber, and some plastics
    Pressurized water, foam, or multi-purpose dry chemical extinguishers should be used
    Never use carbon dioxide or ordinary dry chemical extinguishers (BC) on a class A fire
  Class B : Involve flammable or combustible liquids
    Gasoline, kerosene, paint, paint thinners , and propane
    These types of fires should be extinguished by using foam, carbon dioxide, ordinary dry chemical, multi-purpose dry chemical and halon extinguishers

## Slide 5: PORTABLE FIRE EXTINGUISHER TRAINING
  Class C: Involve energized electrical equipment
    Such as: appliance, switches, panel boxes, and power tools.
    Carbon dioxide, ordinary dry chemical, multi-purpose dry chemical, and halon fire extinguishers may be used
    Water should NEVER be used on electrical fires
  Class D: Involve certain combustible metals
    Such as: magnesium, titanium, potassium, and sodium
    These metals burn at temperatures high enough to pull oxygen out of other metals sufficient to support combustion
    They may react violently with water or other chemicals
    Dry powder extinguishing agents especially designed should be used

## Slide 6: PORTABLE FIRE EXTINGUISHER TRAINING
Types of Extinguishers
  Extinguisher have color-coded symbols on their faceplate or are marked with ratings such as: AB,BC, or ABC
  Class A and B extinguishers carry a numerical rating that tells how large a fire they can safely extinguish (2-A; 4-B) * The higher the number the heavier the extinguisher

## Slide 7: PORTABLE FIRE EXTINGUISHER TRAINING
  Class C extinguishers have a letter rating “C” to indicate that the extinguishing agent will not conduct electricity (Class C rated extinguishers must also carry a Class A or B rating)
  Class D extinguishers carry only a letter rating indicating their effectiveness on certain amounts of specific materials (magnesium, 5 lbs: sodium, 3 lbs.)

## Slide 8: PORTABLE FIRE EXTINGUISHER TRAINING
How to Use:
  In operating a fire extinguisher, it is helpful to remember the word “PASS”
  (Pull, Aim, Squeeze, Sweep)
    Pull the Pin
    Aim Low (at the base)
    Squeeze the handle (hold the extinguisher upright)
    Sweep from side to side

## Slide 9: PORTABLE FIRE EXTINGUISHER TRAINING
When Not to Fight a Fire:
  Portable extinguishers have their limitations
  Not designed to fight large fires
  Only useful under certain conditions
Do not attempt to fight a fire under the following conditions:
  The extinguisher is not rated for the class fire
  The extinguisher is not large enough to put out the fire
  The fire is spreading beyond the spot where it started
  The fire can block your only escape